## Slide 1: Zephyr OS An open-source RTOS ecosystem for secure, connected IoT solutions
Clark Jarvis (MCU Software and Tools Product Marketer)
October 2026

## Slide 2: Table of contents
Zephyr Project Introduction ( Overview | Ecosystem | Dev Community )
1
Infineon's involvement within Zephyr ( Platinum Membership | TSC )
2
Getting started with Zephyr ( Development Board Support )
3

## Slide 3: Confirmation of prework
Zephyr needs eight command-line tools on Windows - a prework script installs all of them
  cmake, ninja, python, git, wget, 7z, gperf, dtc
Run from a regular, non-admin PowerShell window:
  powershell -ExecutionPolicy Bypass -File .\setup-zephyr-windows-deps.ps1
You're done when verification shows eight [OK] lines
Debug probe software - already installed in this room for ModusToolbox™ classes:
  KitProg3 boards (CY8CPROTO-041TP, KIT_PSE84_EVAL) → Infineon's OpenOCD
  KIT_PSC3M6_EVAL → onboard SEGGER J-Link (needs V9.78 or later)

## Slide 4: Setup Steps - What You'll Need Before You Build
Every attendee leaves this session with a working Zephyr workspace, a toolchain, and your own board blinking
One scheduling fact shapes everything below:
  Setting up a Zephyr workspace pulls about 425 MB over the network and lands as roughly 2.5 GB on disk
  Start the download in the first few minutes of this session
You leave with:
  A workspace holding the training fork of Zephyr and every lab application you need this week
  A toolchain your builds can find, and a programmer that can reach your board
  One blinky, built by you, flashed by you, running on your own board

## Slide 5: First Thing in the Room - Start the Download
Install west, Zephyr's command-line tool:
  pip install west
Create the workspace and start the long pole downloading:
  west init -m https://github.com/ClarkJ-Infineon/devcon-training-2026 devcon-ws
  cd devcon-ws
  west update --narrow
--narrow is not optional - without it west fetches every branch/tag instead of the one pinned commit
~280 MB over the network, landing as ~1.25 GB on disk - leave it running and go listen to the presentation
Full copy-paste commands: the manifest repo's README.md -> Quick start (same URL, viewable on GitHub)

## Slide 6: Zephyr Project Overview
Content in this section is taken from Zephyr marketing collateral

## Slide 7: Zephyr Project
Open-source real time operating system
Developer friendly with vibrant community participation
Built with safety and security in mind
Broad SoC, board and sensor support.
Vendor Neutral governance
Permissively licensed - Apache 2.0
Complete, fully integrated, highly configurable, modular for flexibility
Product development ready using LTS includes security updates
Certification ready with Zephyr Auditable
Open Source, RTOS, Connected, Embedded
Fits where Linux is too big
Kernel
OS Services
Application Services
HAL
3rd Party Libraries
Zephyr OS

## Slide 8: Use cases for a real-time OS
Industrial IoT
Asset Tracking
Wearables
Automotive
Healthcare
Worker Safety

## Slide 9: Products Running Zephyr Today
zephyrproject.org/products-running-zephyr
Oticon More Hearing Aid | Lildog & Lilcat Pet Tracker | Livestock Tracker | Moto Watch 100 | Samsung Galaxy Ring | Proglove
Adhoc Smart Waste | Google Chromebook | Framework laptop | Keeb.io BDN9 | Hati-ACE | Blackhole™ PCIe AI Accelerator
BLiXT solid state circuit breaker | Aethero Deimos Satellite | PHYTEC Distancer | Laird Connectivity sensors & gateways | BeST pump monitoring | Vestas Wind Turbines

## Slide 10: 1000+ supported boards… and growing
PSOC™ Control C3M5 Evaluation Kit | PSOC™ Edge E84 Evaluation Kit | PSOC™ 6 AI Kit | nRF9160 DK | STM32F746G Disco | M5StickC PLUS
TDK RoboKit 1 | Arduino Portenta H7 | ESP32 | Arduino Nano 33 BLE | Intel UP Squared | Dragino LSN50 LoRA Sensor Node
Microchip SAM E54 Xplained Pro Evaluation Kit | Raspberry Pi Pico | Altera MAX10 | NXP i.MX8MP EVK | Adafruit Feather M0 LoRa | u-blox EVK-NINA-B3
docs.zephyrproject.org/latest/boards
Infineon Boards

## Slide 11: 270+ Sensors Already Integrated
github.com/zephyrproject-rtos/zephyr/tree/main/drivers/sensor
adt7420 adxl345 adxl362 adxl372 ak8975 amg88xx ams_as5600 ams_iAQcore apds9960 bma280 bmc150_magn bme280 bme680 bmg160 bmi160 bmi270 bmm150 bmp388 bq274xx ccs811 | dht dps310 ds18b20 ens210 esp32_temp fdc2x1x fxas21002 fxos8700 grove grow_r502a hmc5883l hp206c hts221 i3g4250d icm42605 icm42670 icm42688 icp10125 iis2dh iis2dlpc | iis2iclx iis2mdc iis3dhhc ina219 ina23x isl29035 ism330dhcx ite_tach_it8xxx2 ite_vcmp_it8xxx2 lis2dh lis2ds12 lis2dw12 lis2mdl lis3mdl lm75 lm77 lps22hb lps22hh lps25hb lsm303dlhc_magn | lsm6ds0 lsm6dsl lsm6dso lsm9ds0_gyro lsm9ds0_mfd max17055 max17262 max30101 max31875 max44009 max6675 mchp_tach_xec mcp9808 mcux_acmp mhz19b mpr mpu6050 mpu9250 ms5607 ms5837 | nrf5 nuvoton_adc_cmp_npcx nuvoton_tach_npcx nxp_kinetis_temp opt3001 pcnt_esp32 pms7003 qdec_mcux qdec_nrfx qdec_sam qdec_stm32 rpi_pico_temp sbs_gauge sgp40 sht3xd sht4x shtcx si7006 si7055 si7060 | si7210 sm351lt stm32_temp stm32_vbat stmemsc stts751 sx9500 th02 ti_hdc ti_hdc20xx tmp007 tmp108 tmp112 tmp116 vcnl4040 vl53l0x wsen_hids wsen_itds
Notes: Temperature, hall effect, humidity, air quality, gyro, infrared array, accelerometer, magnetometer, pressure, fingerprint, light, heartrate, time of flight, gas, …
111 Sensors as of 2022/11/1

## Slide 12: Zephyr Project Governance
Highest technical decision body consisting of project maintainers and voting members
Sets technical direction for the project
Coordinates X-community collaboration
                Sets up new projects
                Coordinates releases
                Enforces development processes
                Moderates working groups
Oversees relationships with other relevant projects
Governing Board
Decides project goals and strategic objectives
Makes business , marketing and legal decisions
Prioritizes investments and oversees budget
Oversees marketing such as PR/AR, branding, others
Identifies member requirements
Technical Steering Committee
Community
Code base is open to all contributors, need not be a member to contribute.
Path to committer and maintainer status through peer assessed merit of contributions and code reviews
Ecosystem enablement
Goal: Separate business decisions from meritocracy-based, technical decisions
Security Architect
Safety Architect
Individual Contributors
Supporting Organizations
Kernel & Subsystem Maintainers
Security
Oversight
Safety
Oversight
Financial & Policy Oversight
Marketing Oversight
Governing Board
Member Organizations
Others
Architecture Maintainers
Technical Steering Committee
Contributors

## Slide 13: Zephyr Ecosystem
Content in this section is taken from Zephyr marketing collateral

## Slide 14: Zephyr Ecosystem and Architecture
Applications & Middleware
Firmware & Libraries
Governing Board, Technical Steering Committee, Contributors
Training & Consulting
Development Tools
Notes: This is the full Zephyr stack, bottom to top: Hardware Platform, then the Hardware Abstraction Layer, Architecture Interface, Kernel, Low-level OS Services, Connectivity, High-level APIs, and your Application on top. Walk it once bottom-up: the kernel gives you a scheduler, memory management, and timing; OS services add things like file system, settings, crypto, and watchdog; connectivity adds the full protocol ladder from 802.15.4 and BLE up through CoAP, MQTT, and LWM2M; and your application only ever talks to stable high-level APIs above that.
The row to point at for this audience is the Hardware Abstraction Layer, labeled 'SoC vendors' right on the diagram, sitting directly on top of the Hardware Platform row (MCU/MPU, Sensors, Radios, Crypto/Security HW). This is exactly where Infineon plugs in, and it's not just a marketing claim -- the upstream zephyr/soc/infineon tree currently has seven family directories (cat1a, cat1b, cat1c, cat3, edge, psoc4, plus a shared common layer), each mapping to a real product line: PSOC 6, PSOC Control, PSOC Edge, XMC7000, and PSOC 4 all show up at this layer as board and SoC support, not as forks of the OS. Every layer above it, kernel, services, connectivity, is unchanged no matter which Infineon family you're on.
If there's time, briefly name the five ecosystem pillars shown around the architecture (Governing Board/TSC/Contributors, Applications & Middleware, Firmware & Libraries, Development Tools, Training & Consulting) -- Infineon participates as both a contributor at the governance/TSC level and as a downstream silicon vendor shipping board support into the Firmware & Libraries layer.

## Slide 15: Devicetree
Describe & configure the available hardware on the target system
Decouple the application from the hardware
Hardware config lives in Devicetree; software config lives in Kconfig
zephyr,user {
io-channels = <&adc0 12>;
};
aliases {
cmd-pwm = &pwm_cmd;
};
pwmleds {
compatible = "pwm-leds";
pwm_cmd: pwm_cmd_led {
label = "Command PWM (P5.0)";
pwms = <&pwm0_6 0 PWM_USEC(1000)>;
};
};
.overlay file example (KIT_PSC3M6_EVAL)
Notes: Devicetree is how Zephyr describes what hardware actually exists on a board: pins, peripherals, addresses, and how they're wired together, all before any application code runs. The payoff is decoupling: the same driver and the same application code can target different boards because the board's devicetree, not the source code, is what changes.
Infineon angle: in today's advanced labs you will edit a devicetree overlay yourselves. On PSOC Control, the overlay claims the potentiometer's ADC channel and aliases the onboard LED's PWM node so your code can reach them. On PSOC Edge, the overlay is how the display and touch controller get wired up for the LVGL lab. Same mechanism, different peripherals -- this is touchpoint #1 of three you'll hit in both labs.

## Slide 16: IoT Connectivity Options
Wide variety of communication protocols
  Ethernet, 802.15.4, Thread, LoRa, Bluetooth, CAN bus, …
Core network protocols like IPv6, IPv4, UDP, TCP, ICMPv4, and ICMPv6.
Security (ex. TLS, DTLS, …)
Cloud integration using MQTT, CoAP and HTTP protocols
Over-the-air updates
Device management using OMA LwM2M 1.1 protocol
Notes: Zephyr ships a very wide connectivity menu out of the box: link layers like 802.15.4, Thread, LoRa, BLE, and CAN bus; core IP protocols (IPv4/IPv6, UDP/TCP, ICMP); security via TLS/DTLS; and application-level protocols for cloud and device management (MQTT, CoAP, HTTP, OTA, OMA LwM2M). The point to land: you are not choosing an RTOS and separately shopping for a network stack -- it's already integrated and tested together.
Infineon angle: CAN bus support is one of the more active, broadly maintained areas in the upstream repo for Infineon silicon specifically -- about two dozen merged PRs carry both the 'platform: Infineon' and 'area: CAN' labels, spanning multiple families, not just one board. Today's PSOC Control lab is one concrete example (board-to-board command/telemetry over CAN FD), but the same CAN controller driver is relevant anywhere Infineon ships CAN peripherals -- which, given the automotive/industrial motor-control focus of several families, is a lot of the portfolio, not a one-board special case. BLE and Ethernet/TSN are the other two to call out if time allows: BLE via the AIROC CYW20829 BLE MCU, and Ethernet/TSN via XMC7000's native Ethernet MAC hardware.

## Slide 17: Native IP Stack
Built from scratch, on top of Zephyr native kernel concepts
Dual mode IPv4/IPv6 stack
  DHCP v4, IPv4 autoconf, IPv6 SLAAC, DNS, SNTP
Multiple network interfaces support
Time Sensitive Networking support
BSD Sockets-based API
Supports IP offloading
Compliance and security tested
Notes: This is Zephyr's own IP stack, not a third-party add-on: dual-mode IPv4/IPv6, the usual autoconfiguration protocols (DHCPv4, SLAAC, DNS), multiple network interfaces at once, a BSD Sockets API so networking code looks familiar, and IP offloading so chips with their own on-board IP stack (common on Wi-Fi/cellular modules) can be used transparently through the same socket calls.
Infineon angle: the Time Sensitive Networking support called out here is directly relevant to XMC7000's native Ethernet hardware -- TSN and precision time protocol are squarely in the industrial Ethernet and motor-control networking space Infineon targets with that family. Whether you get there over AIROC Wi-Fi or XMC Ethernet, it's the same socket API and the same IP stack underneath.

## Slide 18: Bluetooth Low Energy Controller
Bluetooth 5.3 compliant and qualified (5.1)
Support for multiple BLE radio hardware architectures
Proprietary radios (downstream only)
Unlimited role and connection count
Concurrent multi-protocol support ready
Multiple advertiser and scanner instances
Notes: Zephyr includes one of only a handful of open-source Bluetooth Controller stacks in the industry, 5.3 compliant, supporting multiple radio hardware architectures with unlimited roles and connections, and built to run multi-protocol concurrently (BLE alongside 802.15.4 on the same radio, for example).
Infineon angle: this isn't abstract -- the AIROC CYW20829 BLE MCU on the board list in this deck is a concrete example of this exact open-source controller running on Infineon silicon. If anyone asks 'does Infineon actually ship boards that use Zephyr's own BLE stack, not a vendor blob,' CYW920829M2EVK-02 is the answer.

## Slide 19: Zephyr USB Device Stack
USB 2.0 & USB-C support
Supports multiple MCU families (PSOC Edge, STM32, Kinetis, nRF, SAM,…)
Supports most common devices classes: CDC, Mass Storage, HID, Bluetooth HCI over USB, DFU, USB Audio, etc.
Tight integration with the RTOS
Native execution support for emulated development on Linux
WebUSB support
Notes: USB 2.0 and USB-C support, a broad set of standard device classes (CDC, Mass Storage, HID, DFU, Bluetooth HCI over USB, USB Audio), and -- a nice developer-experience detail -- native execution support, so you can develop and test USB device code on native_posix on your Linux dev machine before ever touching real hardware.
Infineon angle -- this slide's own bullet list (STM32, Kinetis, nRF, SAM) is generic Zephyr marketing collateral and was out of date for an Infineon-hosted session, but the underlying driver support is further along than that bullet list suggests and changed very recently: PR #106841 enabled the shared USB Device Controller (UDC) driver on Infineon PSE84 (PSOC Edge E84) devices, merged April 2026; and PR #113279 added the vendor quirk for the XMC4xxx SoC family to the same udc_dwc2 driver, merged September 12, 2026, about four weeks before this training. Both ride the shared Synopsys DWC2 USB device controller driver plus a small Infineon-specific 'vendor quirk' layer -- the same shared-core-plus-vendor-glue pattern you saw in the architecture slide. Net effect: this is genuinely two Infineon families with real, current USB device support, and it's worth saying on stage that the slide bullet text just hasn't caught up with the repo yet -- a good one-line credibility moment: 'this changed a month ago, the slide hasn't caught up, the repo has.'

## Slide 20: Power Management
Services aimed at reducing power consumption while preserving responsiveness
Key concepts
  Tickless kernel
  System PM: idle thread, interruptions only for registered events
  Device PM: device drivers can react to PM state changes
Handled by the kernel / Customizable by the user
Automated testing using Twister Power Harness
Notes: Two cooperating layers: System Power Management runs the idle thread and only wakes for registered events (a tickless kernel, so there's no periodic timer tick burning power for nothing), and Device Power Management lets individual drivers react to PM state changes so peripherals can be suspended independently of the whole system. Both are handled by the kernel by default but fully customizable, and Zephyr has automated power regression testing via the Twister Power Harness.
Infineon angle: power management is a cross-portfolio concern, not a PSOC Edge-only story -- every battery- or line-powered Infineon design cares about idle/active duty cycling, from PSOC 4's ultra-low-power niche to PSOC Edge's bursty AI/ML inference workloads to motor control's duty-cycled sensing on PSOC Control. Concretely, as of this week there's an open (not yet merged) upstream PR (#121163) adding KIT_PSC3M5_EVK, today's lab board, to Zephyr's own tests/subsys/pm/power_mgmt_soc test suite, targeting the v4.6.0 LTS milestone -- a sign this is active, current work, not a finished/forgotten feature. I'd present power management as broadly applicable and keep any numbers qualitative on stage rather than quoting specific microamp figures unless those are independently verified for the exact board in front of you.

## Slide 21: Secure boot / Device Management
Leverage MCUboot as secure bootloader
Application binary can be signed/encrypted
  Can use hardware keys
But also:
  Downgrade prevention
  Dependency checks
  Reset and failure recovery
Over-the-air (OTA) upgrades
  OMA LwM2M, Eclipse hawkBit
  Vendor offerings
Notes: Zephyr leverages MCUboot as its secure bootloader: application images can be signed and/or encrypted, optionally backed by hardware keys, with downgrade prevention, dependency checks, and reset/failure recovery built in. On top of that sits the OTA update ecosystem: OMA LwM2M, Eclipse hawkBit, and various vendor-specific offerings.
Infineon angle -- this is a live update, not the same status as when this lab was being scoped: MCUboot support for the PSOC Control board family (PSC3M5) was earlier blocked by a TRNG-init hang. That blocker is now resolved -- PR #115553, 'Add MCUboot support and partition fixes' for KIT_PSC3M5_EVK, merged September 23, 2026 (about three weeks before this training), removed the conflicting MXCRYPTOLITE crypto dependency that was deadlocking TRNG init, added sysbuild MCUboot integration, and fixed the flash partition layout. Today's lab still deliberately uses a plain west flash rather than a signed MCUboot image -- that's a 60-minute classroom scope choice, not a technical limitation anymore, and it's worth flagging back to the lab-prep effort as something that could be added in a future revision now that it's unblocked. Good talking point either way: Zephyr's upstream velocity on Infineon support is fast enough that status call-outs in training content need to be re-checked every few weeks, not treated as fixed facts.

## Slide 22: Hardware security
Cryptography APIs
  Random Number Generation, ciphering, etc.
  Supported by crypto HW, or SW implementation (TinyCrypt)
Trusted Firmware integration
  Firmware verification/encryption
  Device attestation
  Management of device secrets
Notes: Zephyr provides a common crypto API surface, backed either by hardware crypto accelerators where present or by a software implementation (TinyCrypt) where they're not, plus Trusted Firmware integration, firmware verification/encryption, device attestation, and secure management of device secrets.
Infineon angle: Infineon has a long heritage in secure elements and HSMs (OPTIGA, TPM), which is a natural brand fit for this layer of the stack.

## Slide 23: Zephyr Dev Community
Content in this section is taken from Zephyr marketing collateral

## Slide 24: Vibrant and active community of contributors
https://github.com/zephyrproject-rtos/zephyr
Total commits: 155,000+
Total contributors: 3,600+
GitHub stars: 16,754 | Forks: 10,157
Commits in the last 30 days: 3,874
Latest tagged release: v4.4.2 (Aug 2026)
~5.2 commits/hour

## Slide 25: GitHub Community Growth
What this data shows:
Commit activity nearly doubled over the past year
16,756 stars and 10,158 forks - a large, broad-reach open-source community.
Fork-to-star ratio (~61%) is high - many developers are actively building on Zephyr, not just bookmarking it.
github.com/zephyrproject-rtos
Chart: Zephyr commit activity (last 12 months)
| Nov '25 | Dec '25 | Jan '26 | Feb '26 | Mar '26 | Apr '26 | May '26 | Jun '26 | Jul '26 | Aug '26 | Sep '26 | Oct '26
Commits/month (approx.) | 2164 | 1890 | 1938 | 1953 | 1943 | 2568 | 2121 | 2413 | 2973 | 3027 | 3593 | 2276
Chart: GitHub reach: zephyrproject-rtos/zephyr
| Stars | Forks
Count (as of Oct 2026) | 16756 | 10158
Notes: Data freshness: stars/forks and commit activity both change weekly. Before presenting, pull current numbers from api.github.com/repos/zephyrproject-rtos/zephyr (stars, forks) and .../zephyr/stats/participation (weekly commit activity), then re-run the chart-rebuild script with the refreshed figures and today's date as the anchor month. The x-axis labels on the commit-activity chart are calendar months anchored to the presentation date, not a live formula, so they need to be regenerated at the same time as the data.

## Slide 26: Share of voice (search & social mentions) vs. other RTOS projects
Chart: 
| Zephyr Project | FreeRTOS | ThreadX | ARM Mbed | RIOT | NuttX
January 2026 | 984 | 570 | 59 | 3 | 7 | 7
RTOS | Mentions
Zephyr Project | 984 (60%)
FreeRTOS | 570 (35%)
ThreadX | 59 (4%)
ARM Mbed | 3 (0%)
RIOT | 7 (0%)
NuttX | 7 (0%)
January 2026
Chart: 
| Zephyr Project | FreeRTOS | ThreadX | ARM Mbed | RIOT | NuttX
February 2026 | 1100 | 261 | 11 | 0 | 4 | 3
RTOS | Mentions
Zephyr Project | 1.1K (79%)
FreeRTOS | 261 (20%)
ThreadX | 11 (1%)
ARM Mbed | 0 (0%)
RIOT | 4 (0%)
NuttX | 3 (0%)
February 2026
Chart: 
| Zephyr Project | FreeRTOS | ThreadX | ARM Mbed | RIOT | NuttX
March 2026 | 662 | 609 | 181 | 5 | 5 | 0
RTOS | Mentions
Zephyr Project | 662 (45%)
FreeRTOS | 609 (42%)
ThreadX | 181 (12%)
ARM Mbed | 5 (0%)
RIOT | 5 (0%)
NuttX | 0 (0%)
March 2026
Source: Zephyr Project marketing team (search + social listening tool), Q1 2026 snapshot.
Notes: This slide answers 'why does Zephyr matter in the market' with external perception data, not just GitHub activity: Zephyr Project held 60% share of voice in January, spiked to 79% in February (likely a specific news/release event worth checking with the Zephyr marketing contact before naming one on stage), then fell back to 45% in March as FreeRTOS's own mentions jumped sharply (35% to 42%) while Zephyr's raw mention count also dropped (984 to 662). Total market conversation volume also shrank March-over-February (1,379 to 1,462 total mentions is roughly flat, but Zephyr's share fell while FreeRTOS's rose) -- call this a trend to watch, not a settled story, and avoid over-interpreting a single quarter's swing without knowing what drove the February spike or the March narrowing.
This data was provided directly by the Zephyr Project team from their own search/social-listening tool (exact platform not confirmed on this end). Unlike the GitHub stars/forks/commit-activity slide earlier in this section, there is no public API to self-refresh this -- if this slide is reused in a future quarter, request an updated export from the Zephyr marketing contact rather than estimating or reusing stale Q1 2026 numbers.

## Slide 27: Table of contents
Zephyr Project Introduction ( Overview | Ecosystem | Dev Community )
1
Infineon's involvement within Zephyr ( Platinum Membership | TSC )
2
Getting started with Zephyr ( Development Board Support )
3

## Slide 28: Infineon’s Platinum Membership benefits
Industry leadership
Fast track to Technical Steering Committee Participation
Help shape the Safety & Certification Programs
Marketing Opportunities
Member Networking Opportunities
Learning & Engagement

## Slide 29: Infineon supported development boards
20 boards, 7 MCU families - in-tree Zephyr support, newest/most-complete families first
PSOC™ Edge
KIT_PSE84_EVAL - E84 Evaluation Kit
KIT_PSE84_AI - E84 AI Evaluation Kit
PSOC™ Control
KIT_PSC3M6_EVAL - C3M6 Evaluation Kit
KIT_PSC3M5_EVK - C3M5 Evaluation Kit
KIT_PSC3M5_CC2 - C3M5 Connectivity Card 2
AIROC™
CYW920829M2EVK-02 - CYW20829 BLE MCU
PSOC™ 4
CY8CPROTO-041TP - PSOC™ 4100T Plus
CY8CKIT-041S-MAX - PSOC™ 4100S Max
CY8CPROTO-040T - PSOC™ 4000T
CY8CPROTO-040T-AUTO - PSOC™ 4000T AUTO
PSOC™ 6
CY8CKIT-062S2-AI - PSOC™ 6 AI Eval Kit
CY8CPROTO-062-4343W
CY8CKIT-062S4 - PSOC™ 62S4 Pioneer Kit
CY8CPROTO-063-BLE
TRAVEO™ T2G
KIT_T2G-B-H_EVK - Body High Eval Kit
KIT_T2G-B-H-LITE - Body High Lite Eval Kit
KIT_T2G-C2D6M-LITE
XMC™
KIT_XMC72_EVK - XMC7200 Evaluation Kit
XMC47-RELAX-KIT
XMC45-RELAX-KIT

## Slide 30: Infineon targeted support in Zephyr® RTOS Ecosystem
Device Support
Tool Enablement
Software Ecosystem
Ecosystem Engagement
All new MCUs and Connected MCUs include Zephyr support by default at public release, unless explicitly exempted
All applicable Zephyr driver APIs that map to supported device peripheral are supported
Enabled Zephyr APIs make best use of Low-Power, DMA, and Security features available in Zephyr
All mass-market focused development kits are supported directly within Zephyr
Differentiated device capabilities are enabled using Custom APIs, per marketing/product requirements
Code Generation of device configuration / initialization using graphical configuration tools
Ease-of-use assets (videos, documentation, tool extensions, installers) targeting bring-up of Zephyr development environment for Infineon devices
Contribution and/or development of IDE support that fully leverages the Zephyr build environment and enables debugging on Infineon devices
AI assisted documentation and coding optimized with relevant Zephyr content for Infineon devices
Support for standard and applicable Zephyr OS Service, including Cryptography, Device Management, Power Management, TF-M
Support for Device Management DFU/OTA within Zephyr (leveraging MCUBoot)
Support for standard Zephyr connectivity: Zephyr Bluetooth LE Stack/Controller, Zephyr CAN, Zephyr Networking, Zephyr USB
Well documented support for out-of-tree middleware targeting key device differentiated software libraries (Apple Find My, CAPSENSE, Safety Test)
Active Platinum level membership in Zephyr engagement
Increased technical training and expertise across customer support contacts (FAE, AE)
Active contribution on technical steering committees and engagement with community
Targeted Zephyr marketing and advocacy efforts (webinars, meet-ups, conferences, whitepapers, events)
Competitive support
Best-in-Class support

## Slide 31: Understanding the Zephyr release process
Baseline Support Submission
ModusToolbox™ Peripheral Driver Library (PDL)
Zephyr hal module for Infineon assets
Wi-Fi / Bluetooth Connectivity support
Infineon specific modules / binary blobs
SOC / Device support
Kernel and baseline Support
Zephyr Project Git Repo
Development board support
Zephyr Driver API support
Zephyr Driver API support
Zephyr Driver API support
Zephyr Driver API support
Submission to Zephyr community with cursory level review
Baseline support submission to Zephyr community. Requires review and acceptance.
Subsequent submissions to Zephyr community for additional driver support.
Once submissions are approved, support is immediately available within the repository
Periodically Zephyr creates a release tag for all available content
Zephyr support is done via a series of community submissions that are reviewed and merged into the community repository. This process can take 8+ weeks depending on complexity and community bandwidth.

## Slide 32: Infineon Development Roadmap for Zephyr
Zephyr 4.4.2 released August 2026
  Full Device Base support for PSOC™ Edge E84
  Full Device Base support for PSOC™ Control C3
  Expanded peripheral coverage: ADC, PWM, CAN FD, CAPSENSE
Near-term (Q3-Q4 CY2026)
  Continued PSOC™ Control C3 coverage (CAN FD, HPPASS ADC)
  Safety Test Library (IEC 60730) workflow integration
  PSE84 multi-core and TF-M / TrustZone security enablement
  PSOC™ 4 HV family expansion (HVMS, HVPA, 040T-AUTO)
  CAPSENSE™ Zephyr tooling integration
  TRAVEO™ / AURIX™ automotive enablement
  Tool enablement & software ecosystem support across the Infineon Zephyr board fleet

## Slide 33: Understanding ModusToolbox™ and Zephyr
IDE support, including Eclipse IDE, VS Code, and 3rd party IDEs.
Support for GCC, IAR, and Arm compilers using ‘make’ based ModusToolbox™ build system.
Graphical UI configurations tool
Leverages Infineon developed low-level drivers, middleware abstraction, middleware, and code examples.
Enables key partner middleware via ModusToolbox™ & Friends program
Targeted at command-line users with some community support for VS Code.
Default support for GCC compiler using ‘west’ based Zephyr build environment. Additional toolchains are now being supported.
Text-based configuration via Kconfig
Leverages vendor provided device support; Infineon support based on low-level drivers.
Community contributed middleware, with support for Zephyr defined driver API, stacks, and RTOS.
Provides a targeted ecosystem focused on development of Infineon devices.
Provides a community driven ecosystem with support for a targeted set of MCUs from a wide range of silicon providers.

## Slide 34: Setup Checkpoint - Toolchain & Finishing the Workspace
Once the download finishes, install the Zephyr SDK:
  west sdk install -t arm-zephyr-eabi
Picks the right SDK version automatically, installs only the ARM toolchain, and registers itself so every future build finds it
Finish with three short commands:
  pip install -r devcon-training-2026/requirements-devcon.txt
  west config build.cmake-args -- "-DOPENOCD=<Infineon OpenOCD path>"
  west patch apply (graphics-lab fixes)
Notes: Pip install line updated 2026-10: the manifest repo now ships its own requirements-devcon.txt at the repo root, which chains Zephyr's own requirements-base.txt (devicetree/Kconfig/west tooling) plus imgtool (MCUboot image signing - also pulls in the cryptography stack TF-M needs) plus jinja2/setuptools. Deliberately NOT zephyr/scripts/requirements.txt - that is Zephyr's own CI umbrella file and pulls in opencv-python, scipy, numpy, pyocd, spsdk, Pillow, plotly, mypy, pylint, clang-format - about 184 MB of wheels this training never uses. If anyone asks why there are two requirements files in a Zephyr workspace, that's why.

## Slide 35: Table of contents
Zephyr Project Introduction ( Overview | Ecosystem | Dev Community )
1
Infineon's involvement within Zephyr ( Platinum Membership | TSC )
2
Getting started with Zephyr ( Development Board Support )
3

## Slide 36: The Pieces of Your Dev Environment
west - meta-tool & package manager
west.yml - manifest, pins every version
Zephyr repo - the RTOS source itself
Zephyr SDK - cross-compilers & debug tools (separate install)
Python + pip - runs west, Kconfig, devicetree tooling
west build → CMake + Ninja → one flashable image
west
meta-tool / package manager
west.yml
manifest - pins versions
Zephyr repo
kernel, drivers, boards, samples
Zephyr SDK
cross-compilers, debug tools
Python + pip
west, codegen, Kconfig tooling
west build
drives CMake + Ninja + codegen
One flashable image
source + devicetree + Kconfig, compiled together
Notes: Four separate things combine into a working Zephyr setup, and it's worth knowing what each one is actually for before we start building.
West is the meta-tool and package manager - it reads a manifest file and fetches or updates everything else below it.
The west manifest, west.yml, pins exact versions: the Zephyr repo itself, plus every HAL and module it depends on, like hal_infineon and mbedtls.
The Zephyr repo is the RTOS source itself - kernel, subsystems, drivers, board and SoC definitions, samples. This is what west init and west update fetch.
The Zephyr SDK is a separate download via west sdk install - cross-compilers, binutils, host debug tools. It is NOT fetched by west update; it's its own step, and a common gotcha for first-time setups.
Python and pip packages matter too - west itself is a pip package, and build-time scripts for devicetree tooling, Kconfig tooling, and imgtool need their own requirements-base.txt install.
How it all ties together: west build drives CMake and Ninja, which call the Python codegen scripts and the SDK toolchain to turn your source, devicetree, and Kconfig choices into one flashable image. That's the single sentence to anchor the whole diagram.

## Slide 37: Zephyr Repository - Where Things Live
boards/<vendor>/<board>/ - board-level support
soc/<vendor>/<family>/ - SoC-level support
dts/bindings/ - devicetree property schema
drivers/ - peripheral drivers
subsys/ - BLE, networking, shell, filesystems
samples/ and tests/ - ready-to-build examples
include/zephyr/ - public API headers
scripts/ - west / Kconfig / DT tooling
zephyr/
boards/<vendor>/<board>/
board-level support
soc/<vendor>/<family>/
SoC-level support
dts/bindings/
schema for DT properties
drivers/
peripheral drivers
subsys/
BLE, net, logging, shell, fs
samples/ and tests/
example apps + test suite
include/zephyr/
public API headers
scripts/
west / Kconfig / DT tooling
Notes: This is the folder-level map of the Zephyr tree attendees already have checked out from the intro session - point at the actual folder in VS Code's explorer if you have it open.
boards/<vendor>/<board>/ is the board-level support - literally what you plug the USB cable into. Every board we use this week (KIT_PSC3M5_EVK, PSOC Edge boards) lives under boards/infineon/.
soc/<vendor>/<family>/ is SoC-level support - the chip itself, shared across every board that uses that chip family, separate from the board wiring.
dts/bindings/ is the schema for every devicetree property a driver understands - this is what makes a property like io-channels valid or invalid, and it's worth a quick look before the devicetree touchpoint lab.
drivers/ holds the actual peripheral drivers - adc, pwm, can, gpio, sensor, and so on - used by any board that exposes that peripheral.
subsys/ is everything built on top of the driver layer: Bluetooth, networking, logging, shell, file systems, device management.
samples/ and tests/ are the ready-to-build example applications and the automated test suite - the next slide is a guided tour of the samples folder specifically.
include/zephyr/ is the public API headers every application #includes - this is the header set IntelliSense/clangd will index.
scripts/ is the Python tooling behind west, Kconfig, and devicetree generation - this is what's actually running under the hood every time you type west build.

## Slide 38: Anatomy of a Board Support Package (BSP)
Same file set, every board
board.yml - identity (board, vendor, SoC)
<board>_defconfig - board Kconfig defaults
<board>.dts + pinctrl.dtsi - devicetree + pin muxing
board.cmake - flash/debug runner
doc/index.rst - Getting Started page
Your overlay ADDS to this, doesn't replace it
boards/infineon/<board>/
board.yml
identity: board, vendor, SoC(s)
<board>_defconfig
board Kconfig defaults
<board>.dts + pinctrl.dtsi
devicetree + pin muxing
board.cmake
which runner flashes/debugs
doc/index.rst
the board's Getting Started page
Your overlay ADDS to this
folder - it does not replace it.
Notes: Every board folder, boards/infineon/<board>/, is the same handful of files no matter which board you pick - once you've seen one BSP you can navigate any of them.
board.yml is pure identity: board name, vendor, and which SoC or SoCs it carries.
<board>_defconfig (or Kconfig.defconfig) is the Kconfig choices this specific board turns on by default - these are the board-level defaults that get merged in later, on the Kconfig tracing slide.
<board>.dts plus <board>-pinctrl.dtsi is the devicetree: what hardware physically exists on the board and how pins are muxed to peripherals.
board.cmake tells west which runner flashes and debugs this board - jlink, openocd, and so on - and how.
doc/index.rst is the board's own Getting Started page in the Zephyr docs - worth bookmarking per board.
The key point to land here: your lab's boards/<board>.overlay is YOUR application adding to this file set, not replacing it. The overlay is applied on top of the board's existing devicetree, which is exactly what the devicetree touchpoint does this afternoon.

## Slide 39: Anatomy of a Zephyr Application
CMakeLists.txt - where your source lives
prj.conf - your Kconfig choices
boards/<board>.overlay - your devicetree additions
src/ - your application code
Same shape, every app, every board
my_app/
CMakeLists.txt
where your source lives
prj.conf
your Kconfig choices
boards/<board>.overlay
your devicetree additions
src/main.c
your actual application code
Same four-file shape, every app, every board -
nothing here is Infineon-specific.
Notes: Every lab you build this week, on either board, follows the exact same four-file shape - this is worth memorizing because it never changes.
CMakeLists.txt tells the build system where your source lives - usually just a one-line target_sources call.
prj.conf is your application's own Kconfig choices - which subsystems are turned on, independent of what the board or SoC already defaults to.
boards/<board>.overlay is your devicetree additions for this specific board - this is the file the devicetree touchpoint edits this afternoon.
src/ is your actual application code - main.c and anything else you add.
Land the takeaway clearly: nothing here is Infineon-specific. This is the same shape for every Zephyr application, on every board, from any vendor. Once attendees know this shape, they can read any sample in zephyr/samples/ the same way.

## Slide 40: Sample Applications - A Guided Tour
hello_world, basic/* - zero/low-dependency smoke tests (blinky, button, fade_led)
subsys/shell/shell_module - interactive console shell
drivers/* - 70+ peripheral demos: adc, can, pwm, i2c, spi, watchdog, counter...
sensor/* - ~75 vendor sensor demos, plus sensor_shell for any supported sensor
subsys/* - usb, usb_c, fs, settings, zbus, modbus, canbus, logging
bluetooth/* - ~90 BLE central/peripheral/mesh samples
net/* - sockets, MQTT, CoAP, HTTP client/server
boards/infineon/ - Infineon's own in-tree sample (autanalog)
Check sample.yaml → platform_allow for board support
Notes: zephyr/samples/ ships hundreds of ready-to-build examples. Most are not relevant to us today, but a handful are worth knowing by name because they build on almost any board, Infineon boards included.
hello_world exercises the entire lab flow - west build, west flash - with zero peripheral dependencies. It's the fastest way to prove your toolchain and flash chain work at all.
basic/blinky drives one GPIO LED - the 'did my board/toolchain/flash chain work at all' smoke test, one step up from hello_world.
basic/button is blinky's counterpart on the input side - GPIO input instead of output.
basic/fade_led is PWM output - this is structurally what this afternoon's lab builds on, so it's worth a quick look before the lab starts.
subsys/shell/shell_module gives you an interactive command shell over the console UART - works on virtually every board, and useful for poking at a running system without rebuilding.
drivers/adc and drivers/can are the two samples closest to today's lab content - ADC read and CAN send/receive - on any board that has those peripherals.
If you want to go further on your own: every sample's sample.yaml lists which boards and platforms it's known to build on, via the platform_allow key - that's the fastest way to confirm a sample will build on your specific board before you try it.
Broadened 2026-10 with more of the catalog beyond basic/: sensor/ ships around 75 samples, almost all vendor-specific drivers for a named part (bme280, lsm6dso, etc.), but sensor_shell is generic - it talks to whatever sensor the board's devicetree exposes, which makes it the fastest way to confirm a sensor is alive on any board, Infineon's included. subsys/ also has usb, usb_c, fs, settings, zbus and modbus samples worth knowing by name even though none are in today's lab. bluetooth/ is the single largest sample category in the tree, around 90 samples covering central, peripheral and mesh roles - call out that most Infineon boards with a BLE radio can run these directly. net/ demonstrates the full networking stack (sockets, MQTT, CoAP, an HTTP client and server) for anyone whose board has an Ethernet or WiFi interface - not relevant to the CAN lab, but worth knowing it's there. boards/infineon/ is worth a specific callout: Zephyr ships at least one sample contributed by Infineon itself (autanalog, an autonomous analog subsystem demo) - proof the vendor samples tree isn't purely upstream community work.

## Slide 41: The Three Touchpoints – Preview of upcoming labs
Devicetree - edit overlay node
Module import - add Kconfig
Code - write real app logic
1
Devicetree
edit an overlay node to claim a peripheral
2
Module import
add the Kconfig for a driver subsystem
3
Code
write the real app logic that uses them
One working peripheral, end to end
you just did all three in miniature
Notes: This slide is a deliberate recap, not new content - the goal is for attendees to recognize the pattern they just saw across the last three slides, named explicitly, before they go build it for real.
Every lab this week, PSOC Control and PSOC Edge alike, hits the same three touchpoints: devicetree - edit an overlay node to claim a peripheral; module import - add the Kconfig for a driver subsystem; code - write the real application logic that uses them.
Land the close explicitly: you just saw all three in miniature, on this screen, over the last three slides. This afternoon, you'll do them for real, on your own board. This is the bridge sentence into the hands-on lab - use it as the transition cue to move attendees from slides to hardware.

## Slide 42: Devicetree - Your First Touchpoint
Board = what hardware exists
Overlay = what your app uses
Reference from PSOC™ Control CAN lab:
zephyr,user {
// TODO 1a: uncomment to claim the pot's ADC channel
io-channels = <&adc0 12>;
};
aliases {
// TODO 1b: uncomment to alias the PWM LED node
cmd-pwm = &pwm_cmd;
};
// TODO 1b: uncomment this whole pwmleds block
pwmleds { compatible = "pwm-leds"; ... };
board.dts + your overlay
+ dts/bindings/ schema
merged devicetree
build/zephyr/zephyr.dts
devicetree.h
generated DT_* macros
your driver / app code
e.g. adc_channel_setup(...)
Notes: This is touchpoint one of three for every lab this week. The distinction to land clearly: the board's own devicetree describes what hardware physically exists; your overlay describes what your specific application actually uses from that hardware.
What's on screen is the literal skeleton attendees will edit this afternoon for the PSOC Control CAN lab - walk through each TODO: uncommenting the ADC channel claims the potentiometer, uncommenting the PWM alias and the pwmleds block claims the onboard LED for PWM brightness control.
Use the diagram on the right to walk the full chain: your board.dts plus your overlay, merged against the dts/bindings/ schema, produces the merged devicetree at build/zephyr/zephyr.dts, which generates the DT_* macros in devicetree.h, which your driver and application code actually calls against - e.g. adc_channel_setup(). If something doesn't build, this is the chain to walk backwards through.

## Slide 43: Kconfig - Your Second Touchpoint
Kconfig = which subsystems get compiled in
prj.conf = your choices, merged with board defaults
Examples from this week's lab:
  CONFIG_CAN=y
  CONFIG_ADC=y
  CONFIG_PWM=y
menuconfig / guiconfig - browse & search interactively
Merge order: SoC → board → prj.conf → extra fragments
Verify build/zephyr/.config, not just prj.conf
Use west build -t menuconfig to check
1. SoC Kconfig.defconfig
silicon-level defaults
2. Board Kconfig.defconfig
board-level defaults
3. Your application's prj.conf
your explicit choices
4. Extra fragments
-DEXTRA_CONF_FILE=... overrides
build/zephyr/.config
the ACTUAL merged, resolved config
A symbol can still be disabled if a
dependency isn't met - verify with
west build -t menuconfig
Notes: This is touchpoint two. Kconfig controls which driver subsystems and OS features actually get compiled into your image - it's a different axis from devicetree: devicetree says what hardware exists, Kconfig says what software support you're turning on for it.
prj.conf is your application's own Kconfig choices, merged with the board's defaults at build time - we'll see exactly how that merge happens on the next slide.
Walk the real example from this week's PSOC Control lab on screen: CONFIG_CAN=y is already enabled as the shared baseline both roles need. CONFIG_ADC=y and CONFIG_PWM=y are each a TODO - attendees need to add these themselves to read the potentiometer and drive the PWM brightness output. This is the Kconfig/driver-import touchpoint in the three-touchpoint framing.
Close with the practical tool: menuconfig or guiconfig let you browse and search every CONFIG_ symbol and its dependencies interactively - show it live if you have a terminal up, it's worth attendees seeing the real TUI before they need it themselves.

## Slide 44: Code - Your Third Touchpoint
API docs: docs.zephyrproject.org/latest – full Doxygen reference
Headers: include/zephyr/<subsystem>/*.h – the real function signatures
Pattern from this week's lab:
  DEVICE_DT_GET(DT_CHOSEN(zephyr_canbus))
  device_is_ready(can_dev)
  LOG_ERR("CAN device not ready")
device_is_ready() - confirms the driver actually initialized, before you touch it
Logging: LOG_INF / LOG_WRN / LOG_ERR instead of printk for anything you ship
Check the return value - almost every Zephyr API returns a negative errno on failure
A dropped return code: Zephyr's #1 time sink
1. docs.zephyrproject.org
API & subsystem reference
2. include/zephyr/*.h
the function signatures you'll call
3. DEVICE_DT_GET + device_is_ready()
get a handle, confirm it initialized
4. Call the driver API
e.g. adc_read(), can_send(), pwm_set_dt()
LOG_INF / LOG_ERR
see it happen on the console, not just printk
Check the return value
almost every Zephyr API returns a negative errno on failure
Notes: This is touchpoint three: Code. Devicetree says what hardware exists, Kconfig says what software support is compiled in, and this is where attendees write the application logic that actually uses both.
Start with where to look things up: docs.zephyrproject.org/latest has the full Doxygen API reference plus subsystem guides, and is the fastest way to find a function signature without grepping. The headers under include/zephyr/<subsystem>/ are the ground truth if the docs are ever behind - worth telling attendees to open the header, not just the web page, when in doubt.
The code on screen is the real pattern from this week's PSOC(TM) Control CAN lab (command_node.c): get a handle with DEVICE_DT_GET at compile time, confirm it actually initialized with device_is_ready() at runtime, then call the driver API. This get-handle / check-ready / call pattern is the same shape for every Zephyr driver, not just CAN.
Close on two habits that save debugging time: use the logging subsystem (LOG_INF/WRN/ERR) instead of printk once code leaves the toy-example stage, and always check the return value - nearly every Zephyr API returns a negative errno on failure, and a silently-dropped error code is the single most common cause of 'it built fine but did nothing' bug reports.

## Slide 45: Key reference links for Zephyr and Infineon MCU
Infineon Zephyr RTOS Discord Channel
Getting Started with:
CY8CPROTO-041TP (PSOC™ 4100T Plus)
KIT_PSC3M6_EVAL (PSOC™ Control C3M6)
KIT_PSE84_EVAL (PSOC™ Edge E84)
Zephyr RTOS GitHub Repository
Infineon Zephyr RTOS Product Page
PSOC™ 6 and Zephyr Video Tutorial

## Slide 46: Build & Flash Blinky - Prove the Chain Works
Your kit | Board target | Clean build time
CY8CPROTO-041TP (PSOC™ 4100T Plus) | cy8cproto_041tp | ~2 minutes
KIT_PSC3M6_EVAL (PSOC™ Control C3M6) | kit_psc3m6_evk | ~1.5 minutes
KIT_PSE84_EVAL (PSOC™ Edge E84) | kit_pse84_eval/pse846gps2dbzc4a/m55 | ~4 minutes (needs --sysbuild)
west build -b <board> -d build/blinky -s zephyr/samples/basic/blinky
  PSOC™ Edge needs --sysbuild (for CM55 builds) - the build succeeds, but without it nothing starts the core
west flash -d build/blinky
  Success = a memory usage report ending the build, and a blinking LED

## Slide 47: If Something Goes Wrong
'west' is not recognized → reopen your terminal; pip install west did not land on PATH
west: unknown command "sdk" → west update has not finished, or you're not inside devcon-ws
ERROR: board <name> not found → typo in the board target, or running from outside devcon-ws
Build succeeds, west flash can't find OpenOCD → the west config line from Setup is missing or wrong
Build succeeds, flash succeeds, no LED (PSOC™ Edge) → you left out --sysbuild
west update stops partway → network issue; run west update --narrow again, it resumes

## Slide 48: Working in VS Code with Zephyr
west on the command line is the one skill every attendee needs - but a good editor still earns its keep:
  Syntax highlighting for devicetree (.overlay) and Kconfig (prj.conf)
  One-click build/flash/debug instead of retyping commands
Two supported paths today - pick based on how much you want VS Code to manage for you:
  Option A - Ac6 Zephyr Workbench: one extension, manages SDK/toolchain/build/flash/debug
  Option B - lightweight extensions: better editing only, you keep driving west yourself

## Slide 49: Option A - Ac6 Zephyr Workbench (full IDE)
Install Ac6.zephyr-workbench from the VS Code Marketplace
Open your devcon-ws folder - it auto-detects the workspace, Zephyr SDK, and Infineon boards, no manual import needed
Validated in hands-on testing:
  Infineon boards appear in the board picker out of the box (no BOARD_ROOT config needed)
  Debug-tools installer fetches Infineon's real ModusToolbox™ Programming Tools - not a reimplementation
  Good clangd defaults: auto-wires the Zephyr SDK toolchain, disables the conflicting default IntelliSense engine
Known rough edges to plan for:
  OpenOCD/J-Link installers need UAC admin rights - may be blocked on locked-down laptops
  No bundled Kconfig support - add luveti.kconfig separately (not trond-snekvik.kconfig, which is Nordic-branded)
  A per-app venv path bug is non-fatal only if you already have system Python on PATH

## Slide 50: Option B - Lightweight Extensions-Only Path
For attendees comfortable with west on the command line who just want a better editor
Install these three extensions:
  clangd - IntelliSense (disable the default C/C++ extension's engine to avoid conflicts)
  KyleMicallefBonnici.dts-lsp - devicetree/.overlay syntax highlighting
  luveti.kconfig - Kconfig syntax highlighting (vendor-neutral)
Wrap west build / west flash in a simple VS Code task (tasks.json) if you want a button instead of typing commands
No SDK/toolchain management, no board auto-detection - you're still driving west yourself, just with a nicer editor